## Slide 1
BLM Update of Gas/
Oil Measurement
Vernal, UT
August 8, 2017

## Slide 3
The New Rules
3173 – Site Security, FMP, Commingling, Off-lease measurement
3174 – Oil Measurement
3175 – Gas Measurment
3178 – Royalty Free Use
3179 – Waste Prevention
All rules became effective on January 17, 2017

## Slide 4
Outline
Overview of the new rules
Timing for Implementation
Facility Measurement Point (FMP)
Variances and Equipment Approvals
Recordkeeping
End-of-month inventories
Commingling
Oil Measurement
Gas Measurement

## Slide 5
Why did we promulgate these rules?
Incorporate latest industry standards
Provide a mechanism to nationally approve new measurement technology/procedures
Provide a mechanism to regularly update industry standards incorporated by reference
Automatically allow automatic tank gauging and Coriolis meters
Define what meters the BLM cares about
Address gaps in the Onshore Orders
Findings from GAO, OIG, RPC

## Slide 6
A Readers Guide…
Subpart 3174 (Onshore Order 4): Oil Measurement
Subpart 3175 (Onshore Order 5, Statewide NTLs for electronic flow computers): Gas Measurement
Subpart 3173 (Onshore Order 3): Site security, FMP, Commingling, Off-lease measurement
Subpart 3170: Definitions, recordkeeping, bypass and tampering, variances, appeals, enforcement

## Slide 7
43 CFR Part 3170
Subpart 3174 (Onshore Order 4): Oil Measurement
Subpart 3175 (Onshore Order 5, Statewide NTLs for electronic flow computers): Gas Measurement
Subpart 3173 (Onshore Order 3): Site security, FMP, Commingling, Off-lease measurement
Subpart 3170: Definitions, recordkeeping, bypass and tampering, variances, appeals, enforcement

## Slide 8
Regulation
Preamble
Procedural
Matters
43 CFR subpart 3175

## Slide 9
Congressional Review Act
Allows Congress to “nullify” final regulations
“Fast Track” Process:
  House passes “Resolution of Disapproval”
  Senate passes “Resolution of Disapproval”
  President signs Resolution
Importantly, the CRA gives the Senate 60 session days in which it may pass a disapproval resolution by simple majority. The 60-session-day period will end in early May
Agency prohibited from ever issuing a rule that is substantially the same without Congressional approval

## Slide 10
Executive Order
All 3170 rules became effective on January 17, 2017
Requires BLM to review regulations
Industry has suggested changes they would like to see
Some of these changes we can handle through policy (IM and enforcement handbook)
Other changes would require a rulemaking

## Slide 11
Promulgating a Regulation (the APA)…
Develop a draft regulation
Develop preamble
Statutes
National Environmental Policy Act
Information Quality Act
Paperwork Reduction Act
Unfunded Mandates Reform Act
Small Business Regulatory Enforcement Fairness Act
Regulatory Flexibility Act
Executive Orders
13211, Actions Concerning Regulations That Significantly Affect Energy Supply, Distribution, or Use
12866, Clarity of the Regulations
13352, Facilitation of Cooperative Conservation
12988, Civil Justice Reform
13175, Consultation and Coordination with Indian Tribal Governments
13132, Federalism
12630, Governmental Actions and Interference With Constitutionally Protected Property Rights (Takings)
12866, Regulatory Planning and Review

## Slide 12
Promulgating a Regulation (the APA)…
Develop a draft regulation
Internal review:
“surnaming”
BLM
Solicitor
Asst. Sec’y
Develop preamble
Revise regulation
Revise preamble
Respond to comments
Internal review:
“surnaming”
BLM
Solicitor
Asst. Sec’y
Regulation is effective
Publish final in
Federal Register
OMB
Publish draft in
Federal Register
OMB
July 2009
January 2017

## Slide 13
Res. Introduced Passed Passed Signed by
Rule No. In House House Senate President
3170/3173 56
3174 82
3175 68
3178/3179 36
Status of Congressional Review Act
www.congress.gov

## Slide 14
Timing for Implementation

## Slide 15
1
2
3
FMP #s
(Existing meters)
>10,000 Mcf/month, >100 bbl/month
1,500 – 10,000 Mcf/month, 10 – 100 bbl/month
<1,500 Mcf/month, <10 bbl/month
Same criteria as FMP
application deadline
3174 Compliance
(Existing FMPs)
High and Very High
Low
Very Low
3175 Compliance
(Existing FMPs)
GARVS
All gas FMPs
Approved Equipment (PMT)
All FMPs
3173/74/75 Compliance (New FMPs)
Nov. 17, 2016
Implementation Time Frames
Jan. 17, 2017
Years

## Slide 16
1
2
3
FMP #s
(Existing meters)
>10,000 Mcf/month, >100 bbl/month
1,500 – 10,000 Mcf/month, 10 – 100 bbl/month
<1,500 Mcf/month, <10 bbl/month
3174 Compliance
(Existing FMPs)
High and Very High
Low
Very Low
3175 Compliance
(Existing FMPs)
GARVS
All gas FMPs
Approved Equipment (PMT)
All FMPs
3173/74/75 Compliance (New FMPs)
Nov. 17, 2016
Implementation Time Frames
Jan. 17, 2017
“new effective date”
Years
Same criteria as FMP
application deadline

## Slide 17
Same criteria as FMP
application deadline
1
2
3
FMP #s
(Existing meters)
>10,000 Mcf/month, >100 bbl/month
1,500 – 10,000 Mcf/month, 10 – 100 bbl/month
<1,500 Mcf/month, <10 bbl/month
3174 Compliance
(Existing FMPs)
High and Very High
Low
Very Low
3175 Compliance
(Existing FMPs)
GARVS
All gas FMPs
Approved Equipment (PMT)
All FMPs
3173/74/75 Compliance (New FMPs)
Nov. 17, 2016
Years
Implementation Time Frames
Jan. 17, 2017
“new effective date”
Lease, CA, or PA basis
Lease, CA, or PA basis
FMP basis

## Slide 18
NMN-16114
1-2
2-2
90 bbl/month
20 bbl/month
1500 Mcf/month
(50 Mcf/day)
900 Mcf/month (30 Mcf/day)
Total oil production:
110 bbl/month
Total gas production:
2,400 Mcf/month

## Slide 19
100 bbl/month
10 bbl/month
3 years
2 years
1 year
Oil
110
10,000 Mcf/month
1,500 Mcf/month
3 years
2 years
1 year
Gas
2,400
Applies to all FMPs on the lease, CA, or PA
FMP Application Deadline
1 year from the “new effective date”

## Slide 20
NMN-16114
1-2
2-2
90 bbl/month
20 bbl/month
1500 Mcf/month
(50 Mcf/day)
900 Mcf/month (30 Mcf/day)
Total oil production:
110 bbl/month
Total gas production:
2,400 Mcf/month

## Slide 21
10,000 Mcf/month
1,500 Mcf/month
3 years
2 years
1 year
Gas
2,400
100 bbl/month
10 bbl/month
3 years
2 years
1 year
Oil
3174 compliance deadline for oil FMPs installed before 1/17/17
1 year from the “new effective date”
110
Applies to all oil FMPs on the lease, CA, or PA

## Slide 22
NMN-16114
1-2
2-2
90 bbl/month
20 bbl/month
1500 Mcf/month
(50 Mcf/day)
900 Mcf/month (30 Mcf/day)

## Slide 23
200 Mcf/day
35 Mcf/day
3 years
2 years
1 year
Gas
3175 compliance deadline for gas FMPs installed before 1/17/17
50
Well 1-2: 1/17/19
30
Well 2-2: 1/17/20
Compliance on an FMP basis, not on a lease basis

## Slide 24
Facility Measurement Point (FMP)
(3170 and 3173)

## Slide 25
3170.3 – Definition
Facility measurement point (FMP) means a BLM-approved point where oil or gas produced from a Federal or Indian lease, unit PA, or CA is measured and the measurement affects the calculation of the volume or quality of production on which royalty is owed. FMP includes, but is not limited to, the approved point of royalty measurement and measurement points relevant to determining the allocation of production to Federal or Indian leases, unit PAs, or CAs. However, allocation facilities that are part of a commingling and allocation approval under § 3173.15 or that are part of a commingling and allocation approval approved after July 9, 2013, are not FMPs. An FMP also
includes a meter or measurement facility used in the determination of the volume or quality of royalty-bearing oil or gas produced before BLM approval of an FMP under § 3173.12. An FMP must be located on the lease, unit, or communitized area unless the BLM approves measurement off the lease, unit, or CA. The BLM will not approve a gas processing plant tailgate meter located off the lease, unit, or CA, as an FMP.

## Slide 26
3170.3 – Definition (simple)
An FMP is a measurement facility that affects the calculation of the volume or quality of production on which royalty is owed, whether or not the BLM has approved it or it has been assigned an FMP number.
An FMP does not include:
Allocation facilities that are part of a commingling approval issued under IM 2013-152 or 3173.14.
Tailgate meters at gas plants that are not located on the lease, CA, or unit PA.

## Slide 27
3173.12(a)(1) – Location
Unless otherwise approved, the FMP(s) for all Federal and Indian leases, unit PAs, or CAs must be located within the boundaries of the lease, unit, or communitized area from which the production originated and must measure only production from that lease, unit PA, or CA

## Slide 28
Why are FMPs Significant?
The regulations (3173, 3174, 3175) primarily apply to FMPs
Operators use the volumes and qualities determined by the FMP for OGOR B/C reporting*
Requires approval from the BLM
Requires an FMP number generated by the BLM
*There may be some exceptions, typically dealing with royalty-free use.

## Slide 29
7,000
1,000
10,000
3,000
2,000
4,000
14,000
9,000
NDM-16113
NDM-16114
25,000
#1
#2
#3
#4
#5
#6
#8
#7
#9
Month of: June 2017
1-1
1-2
1-3
2-1
2-2
2-3
What are the FMP(s) for CA-16114?

## Slide 30
7,000
1,000
10,000
3,000
2,000
4,000
14,000
9,000
NDM-16113
NDM-16114
25,000
#1
#2
#3
#4
#5
#6
#8
#7
#9
Month of: June 2017
1-1
1-2
1-3
2-1
2-2
2-3

## Slide 32
7,000
1,000
10,000
3,000
2,000
4,000
14,000
9,000
NDM-16113
NDM-16114
25,000
#1
#2
#3
#4
#5
#6
#8
#7
#9
Month of: June 2017
1-1
1-2
1-3
2-1
2-2
2-3

## Slide 33
7,000
1,000
10,000
3,000
2,000
4,000
14,000
9,000
NDM-16113
NDM-16114
25,000
#1
#2
#3
#4
#5
#6
#8
#7
#9
Month of: June 2017
1-1
1-2
1-3
2-1
2-2
2-3
Requires off-lease measurement approval

## Slide 35
7,000
1,000
10,000
3,000
2,000
4,000
14,000
9,000
NDM-16113
NDM-16114
25,000
#1
#2
#3
#4
#5
#6
#8
#7
#9
Month of: June 2017
1-1
1-2
1-3
2-1
2-2
2-3
What are the FMP(s) for CA-16113?

## Slide 36
7,000
1,000
10,000
3,000
2,000
4,000
14,000
9,000
NDM-16113
NDM-16114
25,000
#1
#2
#3
#4
#5
#6
#8
#7
#9
Month of: June 2017
1-1
1-2
1-3
2-1
2-2
2-3

## Slide 37
7,000
1,000
10,000
3,000
2,000
4,000
14,000
9,000
NDM-16113
NDM-16114
25,000
#1
#2
#3
#4
#5
#6
#8
#7
#9
Month of: June 2017
1-1
1-2
1-3
2-1
2-2
2-3

## Slide 38
7,000
1,000
10,000
3,000
2,000
4,000
14,000
9,000
NDM-16113
NDM-16114
25,000
#1
#2
#3
#4
#5
#6
#8
#7
#9
Month of: June 2017
1-1
1-2
1-3
2-1
2-2
2-3
Could this be an FMP?

## Slide 39
7,000
1,000
10,000
3,000
2,000
4,000
14,000
9,000
NDM-16113
NDM-16114
25,000
#1
#2
#3
#4
#5
#6
#8
#7
#9
Month of: June 2017
1-1
1-2
1-3
2-1
2-2
2-3
Off-lease measurement and commingling approval

## Slide 40
7,000
1,000
10,000
3,000
2,000
4,000
14,000
9,000
NDM-16113
NDM-16114
25,000
#1
#2
#3
#4
#5
#6
#8
#7
#9
Month of: June 2017
1-1
1-2
1-3
2-1
2-2
2-3
Off-lease measurement and commingling approval

## Slide 41
7,000
1,000
10,000
3,000
2,000
4,000
14,000
9,000
NDM-16113
NDM-16114
25,000
#1
#2
#3
#4
#5
#6
#8
#7
#9
Month of: June 2017
1-1
1-2
1-3
2-1
2-2
2-3
Off-lease measurement and commingling approval
Are these FMPS?

## Slide 42
3170.3 – Definition
An FMP is a measurement facility that affects calculation of the volume or quality of production on which royalty is owed, whether or not the BLM has approved it or it has been assigned an FMP number.
An FMP does not include:
Allocation facilities that are part of a commingling approval issued under IM 2013-152 or 3173.14.
Tailgate meters at gas plants that are not located on the lease, CA, or unit PA.

## Slide 43
7,000
1,000
3,000
2,000
4,000
14,000
9,000
NDM-16113
NDM-16114
25,000
#1
#2
#3
#4
#5
#6
#8
10,000
#7
#9
1-1
1-2
1-3
2-1
2-2
2-3
Compressor
Fuel
1,000

## Slide 44
7,000
1,000
3,000
2,000
4,000
14,000
9,000
NDM-16113
NDM-16114
25,000
#1
#2
#3
#4
#5
#6
#8
10,000
#7
#9
1-1
1-2
1-3
2-1
2-2
2-3
Compressor
Fuel
1,000

## Slide 45
FMPs for Tanks

## Slide 46
1-1
1-3
NMN-25533
Federal Lease
1-2

## Slide 47
1-1
1-3
NMN-25533
Federal Lease
1-2
FMP

## Slide 48
1-1
1-3
NMN-25533
Federal Lease
1-2

## Slide 49
1-1
1-3
NMN-25533
Federal Lease
1-2
1 FMP
1 FMP number
3 unique tank numbers for strapping

## Slide 50
1-1
1-3
NMN-25533
Federal Lease
1-2

## Slide 51
1-1
1-3
NMN-25533
Federal Lease
1-2
3 FMPs
3 FMP numbers
3 unique tank numbers for strapping

## Slide 52
1-1
1-3
NMN-25533
Federal Lease
1-2
An FMP is any tank or tanks that measure a specific color of oil
This is a metaphor

## Slide 53
1-1
1-3
NMN-25533
Federal Lease
1-2
3 FMPs
3 unique tank numbers

## Slide 54
1-1
1-3
NMN-25533
Federal Lease
1-2
3 FMPs
6 unique tank numbers

## Slide 55
1-1
1-3
NMN-25533
Federal Lease
1-2
1 FMP
1 unique tank number
Puce

## Slide 56
1-1
1-3
NMN-25533
Federal Lease
1-2
1 FMP
4 unique tank numbers

## Slide 57
FMPs for LACTs and Gas Meters

## Slide 58
1-1
1-3
NMN-25533
Federal Lease
1-2
FMP (primary)
FMP (secondary)

## Slide 59
1-1
1-3
NMN-25533
Federal Lease
1-2
FMP (primary)
FMP (primary)
Each LACT must have its own FMP number
FMP (secondary)

## Slide 60
1-1
1-3
NMN-25533
Federal Lease
1-2
FMP
FMP
Each gas meter must have its own FMP number

## Slide 61
3173.12 – Applying for an FMP
FMPs are only issued to operators and only operators can apply for an FMP
To comply with the deadlines, an operator’s only obligation is to apply for an FMP
The BLM will send operators a list of leases, CAs, and unit PAs that fall into each category
Gas and oil measurement facilities each have their own FMP number even if they come off the same separator or well

## Slide 62
3173 – FMP Review Process
FMP Application
(simple)
Approve FMP
Issue FMP number
FMP Application
(Comm/OLM)
Grandfathered
(Existing)
Not Grandfathered
Does comm./OLM comply with new regs?
Deny FMP
Rescind/mod approval
Yes
No

## Slide 63
Variances and Equipment Approvals
(3170, 3174, 3175)

## Slide 64
Onshore Orders 4 and 5
Overall concept: Prescriptive requirements for equipment and procedures with opportunity to request meter-specific variances from the local field office.
Oil:
Manual tank gauging
LACT using positive displacement meter
Gas:
Orifice meter with chart recorder
Electronic flow computer (statewide NTLs)

## Slide 65
3174 / 3175
Overall concept: Provide prescriptive measurement procedures as a default with the option for national approval of new or alternative equipment or methods that meet well-defined performance criteria.
Production Measurement Team (PMT):
Central review body for new equipment and procedures
Reviewing specific makes and models of equipment to ensure performance goals are met

## Slide 66
3174 / 3175
Overall concept: Provide prescriptive measurement procedures as a default with the option for national approval of new or alternative equipment or methods that meet well-defined performance criteria.
Oil (default methods):
Manual tank gauging
Automatic tank gauging
LACT with positive displacement meter
LACT with Coriolis meter
Stand-alone Coriolis meter

## Slide 67
3174
Oil (default methods):
Manual tank gauging
Automatic tank gauging
LACT with positive displacement meter
LACT with Coriolis meter
Stand-alone Coriolis meter

## Slide 68
3174/3175
Gas (default methods):
Flange-tapped orifice meter (primary device)
Chart recorders (less than 200 Mcf/day)
Electronic gas measurement (EGM)
Standard methods of gas sampling and analysis

## Slide 69
New Technology
Production Measurement Team (PMT):
Central review body for new equipment and procedures
Reviewing specific makes and models of equipment to ensure performance goals are met

## Slide 70
Approval Process
Operators or manufacturers request approval of a specific make, model, and size of device or a new method
Request includes data – primarily from independent laboratories
PMT reviews data to determine if the device meets performance goals
Recommends approval or denial to the BLM
If approved, the BLM posts that make, model, size of device, or measurement method, on a website
Once posted, any operator can use that device or method with no further review

## Slide 71
www.blm.gov-> Programs

## Slide 72
3170.6 – Variances
Variances are only for meter-specific local issues and are issued by the local field office
Must meet or exceed the performance goals

## Slide 73
Recordkeeping
(3170)

## Slide 74
3170.7 – Recordkeeping
Recordkeeping is the responsibility of lessees, operators, purchasers, transporters, and any other person directly involved in producing, transporting, selling, or measuring oil and gas through the FMP or the point of first sale, whichever is later.
Retention period (generally):
  7 years for Federal leases
  6 years for Indian leases

## Slide 75
3163 – Noncompliance and Civil Penalties
BLM can issue incidents of noncompliance (INC) to and assess civil penalties on “any person”, not just operators
“Any person” includes purchasers and transporters for recordkeeping violations only
“Any person” includes contractors working on behalf on an operator

## Slide 76
End-of-Month Inventories
(3173)

## Slide 77
3173.9 – End of Month Inventory
Required for each lease, CA, PA
Must obtain through gauging (manual or automatic)
Total Observed Volume (TOV):
  Does not have to follow procedures in 3174
  Based only in liquid level and tank strapping table
Timing (Option 1):
±3 days
March
April

## Slide 78
3173.9 – End of Month Inventory
Timing (Option 2):
Derive end of month volume through linear interpolation
March
April
20 days
31 days
V1
V2

## Slide 79
Commingling
(3173)

## Slide 80
Commingling
43 CFR 3162.7-2 -3:
“All measurement…must not be commingled with gas originating from other sources unless approved by the authorized officer under subpart 3173 of this chapter”

## Slide 81
“Source”
Uncommitted Federal/
Indian lease
Federal/Indian CA
Federal/Indian unit PA
State or fee lease
Anything with a case number (e.g. NMN-12345)

## Slide 82
2-1
2-2
2-3
CA: NDM-25211
Not commingling

## Slide 83
1-1
1-2
1-3
2-1
2-2
2-3
3-3
3-4
3-5
Fee
NDM-25211
NDM-25533
Unit Participating Area Approved (NDM-45721A)
Not commingling: no approval needed

## Slide 84
1-1
1-2
1-3
2-1
2-2
2-3
3-3
3-4
3-5
Fee
NDM-25211
NDM-25533
Commingling + Off-lease measurement: approval needed

## Slide 85
3173.12 - Commingling
Conceptually the same as IM 2013-152
Existing commingling approvals are grandfathered if:
  Production is less than 1,000 Mcf/month (gas)
  Production is less than 100 bbl/month (oil)
  Involves downhole commingling

## Slide 86
3173.12 - Commingling
Categories where the BLM can approve commingling:
  Each source has the same percentage of Federal or Indian (same tribe) ownership, same royalty rate, and same revenue distribution
  Economically marginal
  Production is less than 1,000 Mcf/month or 100 bbl/month
  Includes Indian leases and commingling is authorized by tribal law or approved by the tribe
  Downhole commingling in the interest of maximum ultimate recovery
  Overriding considerations

## Slide 87
3173.12 - Commingling
Criteria 1: “Economically marginal”:
  18 month payout (15% ROR in IM 2013-152)
  Based only the commodity commingled
  After tax (before tax in IM 2013-152)
  Explicitly includes taxes, royalties, operating, and variable costs (implicit in IM 2013-152)
  Also qualifies if net present value of royalty over the life of the equipment is less than the capital cost (same as IM 2013-152)
Criteria 2: Capital expenditure greater than NPV of total Federal royalty over the equipment life

## Slide 88
3173 – Other topics
Sealing requirements
Water-draining operations
Hot oiling, clean-up, and completion operations
Report of theft or mishandling of production
Required recordkeeping for inventory and seal records (end-of-month inventory)
Sundry notices
Site facility diagrams
Facility measurement point
Commingling
Off-lease measurement

## Slide 89
Oil Measurement
(3174)

## Slide 90
3174 – Oil Measurement
Performance requirements
  Uncertainty, bias, verifiability
Tank gauging, including automatic tank gauging
LACT systems (PD)
  Temperature averager
Coriolis measurement systems
LACT systems (Coriolis)
Meter proving requirements
  Proving frequency
Measurement tickets
  Required for LACTs and Coriolis
Oil measurement by other methods (PMT)

## Slide 91
Gas Measurement
(3175)

## Slide 92
New
Existing VLV
Existing LV
Existing HV
Order 5, Statewide NTLs, Variances, Written Orders
3175, except GARVS (3175.120(f)) and BLM-approved equipment (3175.40)
3175
1/17/17
1/17/18
1/17/19
1/17/20
EOT
3175.126 (Reporting)
Existing VHV
Application of Regulations – 3175 (Gas)
Grandfathering of meter tubes (A and A’ only) (3175.61(a))
Grandfathering of meter tubes (A and A’ only) and flow computer software (3175.61(b))

## Slide 93
3175 – Gas Measurement
Performance requirements
  Uncertainty, bias, verifiability
Approval of measurement equipment by make and model (after January 17, 2019)
  Transducers
  Flow computer/software
  Flow conditioners
  Differential meters (other than orifice plates)
  Linear meters
  Accounting systems
Orifice meter requirements
Mechanical recorders (< 200 Mcf/day)

## Slide 94
3175 – Gas Measurement
EGM systems (similar to statewide NTLs)
Gas sampling and analysis
Calculation of volume and heating value
Reporting of volume and heating value
  Heating value “dry” unless water vapor measured with laser, chilled mirror, or other BLM-approved device
  Volume cannot be adjusted for water vapor
Testing protocols for transducers and flow computer software

## Slide 95
3175 – Phase-in Periods
Phase-in periods are for “measurement equipment and procedures”
The BLM believes that the requirement for “dry Btus” is a reporting issue, not a measurement equipment or procedure.
Therefore, there is no phase-in period for reporting “dry Btus”

## Slide 96
Contact Information:
3173: Mike Wade (mwade@blm.gov)
303-239-3737
BLM_WO_3173@blm.gov
3174: Beth Poindexter (bpoindexter@blm.gov)
701-227-7724
BLM_WO_3174@blm.gov
3175: Rich Estabrook (restabro@blm.gov)
707-468-4052
BLM_WO_3175@blm.gov
PMT: BLM_WO_PMT@blm.gov